### Functional Design Specification (FDS)
System: Double Acting Cylinder Control using FBD Logic
Platform: Mitsubishi PLC (FBD)
Control Modes: Auto & Manual
Document Type: Stepwise FDS
### 1. System Overview
The system controls a Double Acting Pneumatic Cylinder with two modes: Manual and Automatic.
- Auto Mode: Extends and retracts based on process sequence and interlocks.
- Manual Mode: Allows manual commands for extend/retract.
- Feedback Monitoring: Ensures cylinder reached position with time monitoring.
- Fault Handling: Detects feedback delay to raise faults.
### 2. Inputs and Outputs
#### VAR_INPUT
Tag Name	Data Type	Description
Extend_Cmd	Bit	Command to extend cylinder (Manual or Auto)
Retract_Cmd	Bit	Command to retract cylinder (Manual or Auto)
Extend_FB	Bit	Feedback: cylinder fully extended
Retract_FB	Bit	Feedback: cylinder fully retracted
Auto_Mode	Bit	System in automatic mode
Manual_Mode	Bit	System in manual mode
Interlock	Bit	System permission for movement (safety)
Exend_Rs	Bit	Reset extend fault
Retract_Rs	Bit	Reset retract fault
RESET	Bit	General system reset

#### VAR
Tag Name	Data Type	Description
EX_FB_T	Bit	Timer active for extend FB monitoring
RE_FB_T	Bit	Timer active for retract FB monitoring

#### VAR_OUTPUT
Tag Name	Data Type	Description
Out_Extend	Bit	Output to extend cylinder
Out_Retract	Bit	Output to retract cylinder
Status	Bit	Cylinder is in a valid state (no fault)
Auto_On	Bit	Auto mode status
Manual_On	Bit	Manual mode status
Extend_Fault	Bit	Extend fault if feedback delay
Retract_Fault	Bit	Retract fault if feedback delay
Extend_Fb_Time	Word [Int]	Feedback delay time during extend
Extend_Time	Word [Int]	Total time of extend operation
Retract_Fb_Time	Word [Int]	Feedback delay time during retract
Retract_Time	Word [Int]	Total time of retract operation

### *MANUAL MODE (Extend Operation)
#### 1. Manual Mode Activation
When Manual_Mode bit is ON,
→ System enters Manual Mode.
→ Manual_On output bit is set TRUE.
#### 2. Manual Extend Command Execution
When Extend_Cmd bit turns ON (manual command),
→ AND Manual_On is TRUE,
→ THEN Out_Extend output bit is set TRUE (Cylinder starts extending).
#### 3. Timer Start for Extend Feedback
On activation of Out_Extend,
→ Start a 3-second timer (T_EXT).
#### 4. Feedback Validation within Timer
- If Extend_FB becomes TRUE before T_EXT completes,
  → THEN:
  - Out_Extend is set to FALSE (stop output),
  - Extend_Fb_Time is stored,
  - Status is set TRUE,
    5. Alarm on Feedback Timeout
- If Extend_FB remains FALSE after 3 seconds,
  → THEN:
  - Out_Extend = FALSE,
  - Extend_Fault is set TRUE,
  - Status = FALSE,
6. Alarm Reset Logic
- If Extend_Fault = TRUE,
  → AND Exend_Rs or RESET button is pressed,
  → THEN:
  - Extend_Fault is set to FALSE,
  - System ready for next command.
### *MANUAL MODE (Retect Operation)
### 1. Manual Mode Activation
When Manual_Mode bit is ON,
→ System enters Manual Mode.
→ Manual_On output bit is set TRUE.
#### 2. Manual Retract Command Execution
When Retract_Cmd bit turns ON (manual command),
→ AND Manual_On is TRUE,
→ THEN Out_Retract output bit is set TRUE (Cylinder starts retracting).
#### 3. Timer Start for Retract Feedback
On activation of Out_Retract,
→ Start a 3-second timer (T_RET).
#### 4. Feedback Validation within Timer
- If Retract_FB becomes TRUE before T_RET completes,
  → THEN:
  - Out_Retract is set to FALSE,
  - Retract_Fb_Time is stored,
  - Status is set TRUE,
#### 5. Alarm on Feedback Timeout
- If Retract_FB remains FALSE after 3 seconds,
  → THEN:
  - Out_Retract = FALSE,
  - Retract_Fault is set TRUE,
  - Status = FALSE,
#### 6. Alarm Reset Logic
- If Retract_Fault = TRUE,
  → AND Retract_Rs or RESET button is pressed,
  → THEN:
  - Retract_Fault is set to FALSE,
  - System ready for next command.
### *AUTO MODE (Extend Operation)
#### 1. Auto Mode Activation
When Auto_Mode bit is ON,
→ System enters Auto Mode.
→ Auto_On output bit is set TRUE.
#### 2. Auto Extend Command Execution
- When Extend_Cmd bit turns ON,
  → AND Interlock is TRUE,
  → AND Auto_On is TRUE,
  → THEN:
  - Out_Extend output bit is set TRUE (start cylinder extension),
  - A 3-second timer (T_EXT) is started to monitor extend feedback.
#### 3. Feedback Validation
- If Extend_FB becomes TRUE before T_EXT completes,
  → THEN:
  - Out_Extend = FALSE,
  - Store elapsed time in Extend_Fb_Time,
  - Set Status = TRUE,
#### 4. Fault on Timeout
- If Extend_FB remains FALSE after 3 seconds,
  → THEN:
  - Out_Extend = FALSE,
  - Set Extend_Fault = TRUE,
  - Set Status = FALSE,
  - Message: "Auto Extension Failed – Alarm Set".
#### 5. Alarm Reset Logic
- If Extend_Fault = TRUE,
  → AND Exend_Rs OR RESET is pressed,
  → THEN:
  - Extend_Fault is reset to FALSE,
  - System is ready for next cycle.
### *AUTO MODE (Retract Operation)
#### 1. Auto Mode Activation
When Auto_Mode bit is ON,
→ System enters Auto Mode.
→ Auto_On output bit is set TRUE.
#### 2. Auto Retract Command Execution
- When Retract_Cmd bit turns ON,
  → AND Interlock is TRUE,
  → AND Auto_On is TRUE,
  → THEN:
  - Out_Retract output bit is set TRUE (start cylinder retraction),
  - A 3-second timer (T_RET) is started to monitor retract feedback.
#### 3. Feedback Validation
- If Retract_FB becomes TRUE before T_RET completes,
  → THEN:
  - Out_Retract = FALSE,
  - Store elapsed time in Retract_Fb_Time,
  - Set Status = TRUE,
#### 4. Fault on Timeout
- If Retract_FB remains FALSE after 3 seconds,
  → THEN:
  - Out_Retract = FALSE,
  - Set Retract_Fault = TRUE,
  - Set Status = FALSE,
  - Message: "Auto Retraction Failed – Alarm Set".
#### 5. Alarm Reset Logic
- If Retract_Fault = TRUE,
  → AND Retract_Rs OR RESET is pressed,
  → THEN:
  - Retract_Fault is reset to FALSE,
  - System is ready for next cycle.

### *TIME TRACKING

        1. Extend Feedback Time → Extend_Fb_Time
2. Total Extend Time → Extend_Time
3. Retract Feedback Time → Retract_Fb_Time
4. Total Retract Time → Retract_Time

### Data Register Assignment (example):
Time Value	Tag	Data Register	Format
Extend Feedback Time	Extend_Fb_Time	D100	INT (Word)
Extend Total Time	Extend_Time	D101	INT (Word)
Retract Feedback Time	Retract_Fb_Time	D102	INT (Word)
Retract Total Time	Retract_Time	D103	INT (Word)